## Slide 1
WASTE TO VALUE
Conversion of Vegetable Waste into Organic Plant Pellets
Turning vegetable waste into a useful agricultural resource
♻ Waste Management • 🌱 Agriculture • 🔄 Circular Economy
Tushar Kumar TR

## Slide 2
The Main Problem
Large-scale vegetable & food waste generation
• Organic waste is frequently sent to landfills or mixed with other waste.
• High moisture makes fresh vegetable waste difficult and expensive to transport and store.
• Decomposition produces unpleasant odors and can attract insects and pests.
• Valuable organic matter and nutrients are lost.
• Farmers and gardeners need affordable and easy-to-use organic inputs.
CORE PROBLEM
Valuable nutrients and organic matter from vegetable waste are being discarded instead of being converted into a useful agricultural resource.

## Slide 3
Our Solution
Convert segregated vegetable waste into organic plant pellets
Vegetable Waste
Dehydration
Grinding
Formulation
Pelletization
Quality Testing
Plant Application
♻ Converts organic waste into a useful agricultural input
🌱 Provides organic matter to soil
💧 Reduces moisture and waste volume
📦 Easier to store and transport
🌾 Pellet form makes application convenient
🔄 Supports a circular economy

## Slide 4
Product Development
Complete manufacturing pathway
Collection
Segregation
Size Reduction
Dehydration
Grinding
Formulation
Mixing
Pelletization
Cooling & Screening
Quality Testing
Plant Testing
Packaging

## Slide 5
Step 1 & 2 — Collection and Segregation
COLLECTION SOURCES
Hotels Hostels Restaurants College canteens Vegetable markets Catering facilities
SUITABLE MATERIALS
Vegetable peels • trimmings • fruit residues • spoiled but uncontaminated vegetables • plant-based kitchen residues
AVOID
Plastic • glass • metal • chemicals • excessively oily waste • meat and bones • highly contaminated material

## Slide 6
Step 3 — Size Reduction
Shredding and chopping
PURPOSE
Increase surface area Improve drying efficiency Make material easier to process Produce more uniform final material
Vegetable Waste
Shredder
Small Particles

## Slide 7
Step 4 — Dehydration
Removing excess moisture
POSSIBLE SYSTEMS
☀ Solar dryer Tray dryer Hot-air dryer Industrial continuous dryer
PURPOSE
Remove excess water Reduce spoilage Reduce transportation weight Improve storage stability Prepare for grinding
INNOVATION OPPORTUNITY
Investigate a solar-assisted drying system to potentially reduce energy consumption.

## Slide 8
Step 5 & 6 — Grinding and Formulation
Dried Material
Grinder
Organic Powder
GRINDING
Use a pulverizer or hammer mill. Aim for a relatively consistent particle size for uniform mixing and pelletization.
FORMULATION
The vegetable-waste powder becomes the organic base. Ingredients may be selected to improve nutrient consistency, organic matter, pellet strength, storage stability and soil performance.

## Slide 9
Step 7 & 8 — Mixing and Pelletization
MIXING
Organic powder + formulation ingredients → uniform mixture. Uniform mixing helps each pellet have approximately the same composition.
Powder
Pelletizer
Small Pellets
PELLET SIZE
A 3–6 mm diameter pellet size could be investigated for general soil and nursery applications.

## Slide 10
Step 9 — Cooling & Screening
Producing uniform, strong and easy-to-handle pellets
COOLING
Fresh pellets are cooled after pelletization.
SCREENING
Broken or oversized pellets are separated. Suitable material proceeds as the final product.
TARGET
UNIFORM STRONG EASY TO HANDLE Broken material can potentially be returned to the process.

## Slide 11
Step 10 — Quality Testing
Quality testing before commercial sale
NUTRIENT TESTING
Nitrogen Phosphorus Potassium Organic carbon Moisture pH Electrical conductivity C:N ratio
SAFETY TESTING
Heavy metals Pathogens Physical contaminants
PHYSICAL TESTING
Pellet size Pellet strength Bulk density Moisture stability Breakdown behavior

## Slide 12
Step 11 — Plant-Growth Testing
Generating scientific evidence for product performance
EXPERIMENTAL GROUPS
A — No organic supplement B — Compost C — Basic pellet D — Improved formulation E — Commercial reference product
MEASURE
Germination Plant height Number of leaves Root growth Fresh biomass Dry biomass Soil parameters

## Slide 13
Step 12 — Packaging
Moisture-resistant packaging after successful testing
1 KG
Home gardeners
5 KG
Terrace gardens Nurseries
10 KG
Larger users
25 KG
Farms & professional users
Packaging should clearly state composition, intended use and applicable regulatory information.

## Slide 14
Target Market
Three major customer groups
🌱 HOME GARDENERS
Demand: Easy application • Small packages • Clean product • Low odor • Convenient storage Positioning: “Easy-to-use organic pellets for home plants and kitchen gardens.”
🌿 NURSERIES & LANDSCAPING
Demand: Consistent quality • Convenient application • Bulk packaging • Reliable supply • Predictable specifications
🌾 FARMERS & COMMERCIAL GROWERS
Demand: Cost effectiveness • Nutrient value • Reliable results • Bulk availability • Soil compatibility

## Slide 15
Marketing Strategy
Show the transformation
Hotel Waste
Dried Material
Organic Powder
Pellets
Plant Trial
DEMONSTRATION PLOTS
Provide samples to nurseries and selected growers. Use controlled demonstrations and measurable results rather than unsupported claims.

## Slide 16
Hotel & Hostel Partnership
Turn raw-material suppliers into strategic partners
Hotel
Segregated Waste
Processing Facility
Organic Pellets
Farmers / Gardeners
ADDITIONAL VALUE
A waste-diversion report/certificate could potentially show the amount of organic material recovered, subject to applicable local rules and verification.

## Slide 17
Market Positioning
How should the product be presented?
❌ AVOID
“Fertilizer made from food waste.”
✅ POSITION AS
“A standardized organic plant pellet created by converting segregated vegetable waste into a convenient agricultural input.”
Waste Management
Resource Recovery
Agriculture
Convenience

## Slide 18
Revenue Model
Two potential revenue streams
1 — PRODUCT SALES
Sell pellets to: Nurseries Farmers Gardeners Landscaping companies
2 — WASTE-PROCESSING SERVICE
Hotels, hostels and institutions may potentially pay for or contract collection/processing of segregated organic waste, depending on local arrangements.
Processing Revenue
Pellet Sales
Stronger Business Model

## Slide 19
Competitive Advantage
Why can the product stand out?
♻ WASTE-TO-VALUE
Converts a waste stream into a useful agricultural input.
💧 DEHYDRATED FORMAT
Lower moisture can make material easier to handle.
📦 PELLET FORMAT
Cleaner and easier to apply than loose organic waste.
🔬 STANDARDIZATION
Laboratory testing can provide consistent specifications.
🌱 BIOLOGICAL ENHANCEMENT
Future formulations could investigate suitable beneficial microorganisms.
☀ RENEWABLE-ENERGY PROCESSING
Solar-assisted dehydration could potentially reduce processing energy.

## Slide 20
Complete Business Model
From waste to plant
Hotels / Hostels / Canteens
Vegetable Waste
Sorting
Shredding
Dehydration
Grinding
Formulation
Mixing
Pelletizing
Quality Testing
Packaging
Nurseries / Farmers
Gardeners
Agriculture
Plants
Organic Waste
Recycling

## Slide 21
Final Pitch
“We convert segregated vegetable waste from hotels and hostels into standardized, easy-to-use organic pellets, creating a circular link between food waste management and sustainable plant production.”
WASTE
RESOURCE
AGRICULTURE
SUSTAINABILITY

## Slide 22
THANK YOU
♻ Turning Waste Into Value
🌱 Growing a Sustainable Future
QUESTIONS & DISCUSSION